## Slide 1: Planning for Accessible Meetings
By Nate Crippes and Sheri Newton

## Slide 2: Sources
U.S. Access Board
Department of Justice
Mid Atlantic ADA Center
Web Accessibilty Initiative
Harvard University
Hospitality and Disability: An ADA National Network Initiative

## Slide 3: American with Disabilities Act (ADA)
Physical Accessibility
Parking
Route
Entrance
Signage
Not covered: Restrooms, Passenger Drop-off areas, route from public transportation, etc.

## Slide 4: Parking Spaces Scoping Requirements
(§208)

## Slide 5: Location of Parking Space
On shortest accessible route to accessible entrance
Dispersed to multiple accessible entrances

## Slide 6: Minimum Number of Accessible Spaces
Parking Facility Total | Standard | Van* | Total (Standard + Van)
1 - 25 | 0 | 1 | 1
26 – 50 | 1 | 1 | 2
51 – 75 | 2 | 1 | 3
76 – 100 | 3 | 1 | 4
101 – 150 | 4 | 1 | 5
151 - 200 | 5 | 1 | 6
201 – 300 | 5 | 2 | 7
301 – 400 | 6 | 2 | 8
401 – 500 | 7 | 2 | 9
501 – 1000 | [Total – van] | * | 2 percent of total
1001 – and over | [Total – van] | * | 20, plus 1 for each 100, or fraction thereof, over 1000
* at least 1 of every 6 accessible spaces or fraction of 6

## Slide 7: Parking Scoping - Van Accessible Spaces
1 van space for every 6 accessible spaces required
There will always be at least one van space required

## Slide 8: Parking Spaces Technical Requirements
(§502)

## Slide 9: Surface and Slope
Required to be level
  Both space itself and associated access aisle
Stable, firm, and slip resistant
Slope measured parallel to and perpendicular to the access aisle

## Slide 10: Access Aisle - Location
Cannot overlap vehicle way
Can be shared by two vehicle spaces
Can be on either side of vehicle space
  Access aisle must be on passenger side of van spaces where angled parking is provided
Recommendation: Provide access aisle for vans on the passenger side so that drivers do not have to back into the space

## Slide 11: Access Aisle – Accessible Route
Accessible Route must connect to access aisles at accessible parking spaces
Recommendation: Connect accessible route to front of aisle to prevent travel behind parked cars

## Slide 12: Access Aisle - Size
Width: 60″ minimum
Length: full length of served parking space
60″ min

## Slide 13: Vehicle Space - Width
Measurement taken to center line of marked lines

## Slide 14: Alternate Van Spaces and Access Aisle
Van parking spaces shall be permitted to be 96 inches wide minimum where the access aisle is 96 inches wide minimum.

## Slide 15: Vertical Clearance for Vans
Vans requires at least 98″ of vertical clearance

## Slide 16: Vertical Clearance Location
Minimum clearance applies to vehicular route from entrances to van spaces

## Slide 17: Parking Space Signs
International Symbol of Access required to identify accessible spaces
Signs identifying van spaces must include the term "van accessible”
Exception: sign not required where 4 or fewer spaces are provided on a site

## Slide 18: Parking Space Signs - Height
60 inches minimum to bottom of sign
  Including “Van accessible” signs

## Slide 19: Parking Space Signs – Height Example

## Slide 20: Parallel Parking
All parking requirements still apply

## Slide 21: Temporary Parking Solutions

## Slide 22: Route of Travel Technical Requirements
(§502)

## Slide 23: Route of Travel: inside and outside

## Slide 24: Route considerations
Is the walking surface stable firm and slip resistant?
Is the route free of surface openings greater than ½”
Is the route free of changes in level greater than ½”?

## Slide 25: Route considerations
Is the route at least 36” wide?
Is the running slope less than 5%? (slopes greater than 5% are subject to ramp requirements)
Is the cross slope no greater than 2.08%

## Slide 26: Route considerations – protruding objects
Is the route free of items at the height of 27”-80” that protrude from the wall?
display cases
water fountains
signs
ceiling mounted televisions
drop boxes

## Slide 27: Route Solutions?
Place object (box, cone, trash can) beneath protruding object

## Slide 28: Entrance

## Slide 29: Entrance
Is there one accessible entrance connected with an accessible route?
Is the doorway at least 32”

## Slide 30: Entrance
Is the threshold height less than ½ inch or ¾ inch beveled?
Can the door be opened with a flat palm or closed fist?

## Slide 31: Entrance
Is there 18 inches of clear space on the pull side of the door?
Is there a 60-inch level area in front of the door?

## Slide 32: Entrance Solutions? Prop the door open.

## Slide 33: Signage

## Slide 34: Accessible Entrance
Directions to the entrance
Marking the accessible entrance

## Slide 35: Accessible Entrance
Directions to accessible pathway

## Slide 36: Your Input
What accessibility features are important to your meeting participants?
What have you done to make past meetings more accessible?

## Slide 37: In-Person Meeting Set-Up
Circulation space should be 36 inches and preferably 60 inches. 72” passing space is recommended.
Include both horizontal (side to side) and vertical (front to back aisles to improve access and flow.
Area to park scooters and mobility devices
Accessible locations to sit throughout the room
A spacious area in the back or sides of the room for those who need to stand
Plenty of space between group discussions.

## Slide 38: MEETING SET-UP

## Slide 39: Meeting Set-Up
Was there a greeter offering assistance at the main entrance or meeting room entrance?
Was it clear who to reach out to for help?
Check-in table: room to navigate? appropriate height?
Aisles 60 inches wide
Spaces for wheelchair seating?

## Slide 40: Layout Examples – Theater Style

## Slide 41: Layout Examples – Round Table Style

## Slide 42: During the Meeting
Did speakers use a microphone?
If a video was shown, did it have captions?
If visuals were used, did the speaker describe the visuals?
Did you notice other accommodations: sign language interpreters, large print materials, magnifying sheets or large grip pens?
If multiple groups were meeting in one area, was there an option to move to a different location if the ambient noise was difficult for a participant?

## Slide 43: Voting
How did participants vote?
If paper ballots were used, was there an alternative method available for someone who cannot read or mark a paper ballot?

## Slide 44: Other Meeting Features
ACCOMMODATIONS

## Slide 45: In-Person Meeting Set-Up
Designated person to coordinate accommodation needs
Greeters at the door to assist and lead participants to the right area
Use amplification
Videos should be captioned
Plan for alternative ways voters with physical limitations can participate and vote

## Slide 46: More Meeting Tips and Info
Hospitality & Disability
https://www.adainfo.org/hospitality/accessible-meetings-events-conferences-guide/#tab6
Harvard University
https://accessibility.harvard.edu/event-planning

## Slide 47: VIRTUAL MEETINGS

## Slide 48: VIRTUAL MEETING CONSIDERATIONS
Choosing a Platform
Managing Registration
Arranging for Accommodations
Ensuring Accessiblity
Tips for Presenters and Participants

## Slide 49: Choosing a Platform
Is the software accessible for those who use screen-reading software?
Can third-party captioning be integrated?
Not everyone has access to a computer or reliable internet connection. Does the platform support call in via telephone?
Provide support or in advance instructions for those who need help operating the platform.
Can you pin a screen for the sign language interpreter?

## Slide 50: Registration or Pre-Meeting Communications
Designate an accessibility point person and make his/her phone number and email address available on all event materials
Materials should include specific information about accessibility features available during the event and how to request additional accommodations.

## Slide 51: Sample Language
“Live captioning and American Sign Language interpretation will be available during this event. Should you require any other accommodation or service to fully participate, please contact [NAME at EMAIL, PHONE NUMBER] at least [#] days prior to the event. Participants can log in to the event platform 30 minutes prior to the start of the event for troubleshooting and technology support.”

## Slide 52: Arranging for Accommodations
Event attendees may require a variety of accommodations to participate. It’s important to factor these into your budget. Examples include:
Communication access real-time translation (CART), also called live or real-time captioning
Sign language interpretation
Accessible digital materials
Large print
Provision of event materials in advance to allow for extra time to process information

## Slide 53: Planning for Accessibility
Examples:
Caption and audio-describe any pre-recorded media that will be shared during the event
Avoid media that include bright, flashing lights
Develop accessible presentation materials (such as PowerPoint slide presentations and Word documents) with easy-to-read fonts, contrasting colors, and image descriptions or alternative text
Prior to the event, host a live run-through for presenters, captioners, and interpreters. This can help prevent technical issues and help ensure everyone is on the same page regarding the flow of the event.

## Slide 54: Tips for Presenters and Participants
Use best practices for slides and visuals.
Describe all relevant visual information
Limit chat when a participant is using a screen reader
Speak clearly
Use simple language (avoid acronyms and idioms)
Pause between topics. Give plenty of time for people to process the information and formulate their questions
Be visible, good lighting. Some folks benefit from lip reading.
Repeat items in the chat.
Limit distractions (notifications, side conversations)

## Slide 55: Sheri Newton snewton@disabilitylawcenter.org (800) 662-9080